## Slide 1
KL UNIVERSITY
Design and Simulation of a Digital
Access Verification System
Using XOR / XNOR Logic
BATCH 13
Presented by: Tanish (2620080073) • Vrithika (2620080089) • Sujeet (2620090014) • Prakash (2620080060) • Meghana (2620080049)
Module 1 — Digital Logic Fundamentals
Notes: <number>

## Slide 2
Agenda
1
Introduction to Access Verification Systems
2
Module 1 Recap — Basic Logic Gates
3
XOR Gate — Working & Truth Table
4
XNOR Gate — Working & Truth Table
5
Bit-Comparator Concept for Access Checking
6
System Block Diagram
7
Circuit Diagram (Simulated in Logisim)
8
Applications, Advantages & Conclusion
Batch 13 | KL University
2
Notes: <number>

## Slide 3
What is a Digital Access Verification System?
A circuit that checks whether an ENTERED CODE matches a STORED (authorized) CODE, and grants or denies access based on the result — the same logic used in keypad locks, ID card readers and PIN checks.
1
Input
User enters a binary code (e.g. 4-bit password)
2
Compare
XOR/XNOR gates compare each bit with the stored code
3
Decide
AND gate combines results → output tells match / no match
Batch 13 | KL University
3
Notes: <number>

## Slide 4
Module 1 Recap — Basic Logic Gates
AND
Y = A . B
Output is 1 only if all inputs are 1
OR
Y = A + B
Output is 1 if any input is 1
NOT
Y = A̅
Output is the inverse of the input
XOR
Y = A ⊕ B
Output is 1 only if inputs are DIFFERENT
XNOR
Y = (A ⊕ B)̅
Output is 1 only if inputs are SAME
This project focuses on XOR and XNOR — the two gates used to build the bit comparator.
Batch 13 | KL University
4
Notes: <number>

## Slide 5
XOR Gate
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Boolean Expression: Y = A ⊕ B
In access verification, XOR flags a MISMATCH: if the entered bit and the stored bit are different, XOR outputs 1 (error / no match) for that bit position.
Batch 13 | KL University
5
Notes: <number>

## Slide 6
XNOR Gate
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Boolean Expression: Y = (A ⊕ B)̅
XNOR flags a MATCH: if the entered bit and the stored bit are the SAME, XNOR outputs 1. This is why XNOR is the natural choice for a bit comparator.
Batch 13 | KL University
6
Notes: <number>

## Slide 7
Bit-Comparator Concept for Access Checking
Each bit of the entered code is compared with the corresponding bit of the stored code using an XNOR gate.
Entered Code (A)
1 0 1 1
Stored Code (B)
1 0 1 1
XNOR each bit →
XNOR Result:
1 1 1 1
AND all XNOR outputs together → if the result = 1, EVERY bit matched → ACCESS GRANTED.
If even ONE bit differs, the AND output = 0 → ACCESS DENIED.
Batch 13 | KL University
7
Notes: <number>

## Slide 8
System Block Diagram
Keypad / Switches
(Entered Code)
Stored Code
(Reference Register)
XNOR Comparator
(bit-by-bit)
AND Gate
(final decision)
LED / Buzzer
Output
Two independent inputs (entered code and stored code) are compared bit-wise; the combined result drives a visible/audible output.
Batch 13 | KL University
8
Notes: <number>

## Slide 9
Circuit Diagram — Simulated in Logisim
Batch 13 | KL University
9
Notes: <number>

## Slide 10
Worked Example — 4-bit Code Check
Case 1: Correct Code Entered
Bit | A (Entered) | B (Stored) | XNOR Output
0 | 1 | 1 | 1
1 | 0 | 0 | 1
2 | 1 | 1 | 1
3 | 1 | 1 | 1
AND = 1 → ACCESS GRANTED
Case 2: Wrong Code Entered
Bit | A (Entered) | B (Stored) | XNOR Output
0 | 1 | 1 | 1
1 | 1 | 0 | 0
2 | 1 | 1 | 1
3 | 1 | 1 | 1
AND = 0 → ACCESS DENIED
Batch 13 | KL University
10
Notes: <number>

## Slide 12
Applications
1
Digital door locks & keypad entry systems
2
ATM PIN and card verification circuits
3
Password-protected embedded devices
4
Employee ID / RFID access control panels
5
Vehicle immobilizer / anti-theft systems
6
Secure locker and safe-box mechanisms
Batch 13 | KL University
11
Notes: <number>

## Slide 13
Advantages & Limitations
Advantages
Simple, low gate-count design
Fast comparison — works in real time
Easy to scale to more bits (8, 16...)
Low power and low cost to build
Easy to simulate and test in Logisim
Limitations
Fixed code is hardwired / not easily changed
No encryption — code is compared in plain bits
Vulnerable to physical tampering
Limited to simple match / no-match logic
Batch 13 | KL University
12
Notes: <number>

## Slide 14
Conclusion
1
XOR and XNOR gates provide a simple and reliable way to compare digital codes bit by bit.
2
XNOR's “match = 1” behaviour makes it ideal for building an access/password comparator.
3
Combining XNOR outputs with a single AND gate gives one clean Grant / Deny signal.
4
The design was verified using truth tables and simulated successfully in Logisim.
Batch 13 | KL University
13
Notes: <number>

## Slide 15
KL UNIVERSITY
Presented By — Batch 13
T
Tanish | 2620080073
V
Vrithika | 2620080089
S
Sujeat | 2620090014
P
Prakash | 2620080060
M
Meghana | 2620080049
Digital Access Verification System Using XOR / XNOR Logic | Module 1
Thank You
github.com/tanishsharma73/KLH-FED-2026-SESSION13-BATCH-13
Notes: <number>